## Slide 1
Bonner Bridge Submerged Aquatic Vegetation Mitigation
Phillip Todd (Atlantic Reefmaker)
Mark Fonseca (CSA)
Tyler Stanton (NCDOT)
Western Dredging Association

## Slide 2
BACKGROUND
Bonner Bridge seagrass impacts
Bonner Bridge only direct connection of the NC Outer Banks to the mainland – in severe disrepair and is being replaced
Need 1.28 acres (0.52 hectare) new seagrass for Bonner Bridge impacts
No nearby candidate areas to be “fixed”
Here:
  Apply models of wave energy ↔ seagrass landscapes
  Reduce wave energy on patchy seagrass beds
  ↑Seagrass patch #, expansion, coalescence = increased acreage

## Slide 3
BACKGROUND
Seagrass landscapes change across disturbance gradients
Increasing currents, waves, bioturbation
(disturbance extent, intensity, duration, frequency, sequence)

## Slide 4
BACKGROUND
Tipping points in NC seagrass cover

## Slide 5
APPROACH
Mitigation location and strategy
Oregon Inlet & Bonner Bridge
Dredge material islands

## Slide 6
APPROACH
Forecast seagrass cover response to wave ↓
Seagrass cover f(RWE) before vs after wall
For every foot of wall we forecast ↑ 150 ft2 (13.9 m2) of seagrass
500’ of wall = ~1.7 ac (0.69 ha)

## Slide 7
APPROACH
Mitigation Alternatives Analysis
Eight options
Factors reviewed/ studied
  Mobilization challenges
  Installation issues
  Maintenance concerns
  Costs
  Estimated essential fish habitat (EFH) utility
  Potential site impacts

## Slide 8
IMPLEMENTATION
Installation Dec 2016 – Jan 2017
Excavator pushed 12” diameter fiberglass pile into substrate (~25’ deep)
Installed in Low Draft Conditions
No access channel dug to the installation site

## Slide 9
MONITORING
Installation Dec 2016 – Jan 2017
Δ Biological colonization
Δ Sediment elevation
Δ Seagrass coverage

## Slide 10
RESULTS
Near field sediment elevation survey
Transect surveys of elevation
Erosion pits under structure
Shoaling on south (lee) side

## Slide 11
RESULTS
Near field sediment elevation survey
Substrate % Cover | Infrequent Inundation | Frequent Inundation | Near-continual Inundation
Embedded Granite Rock | 0 | 19 | 17
Concrete Base | 27 | 70 | 90
Concrete base
Embedded rock
~15% areal cover relocated seagrass

## Slide 12
RESULTS
Epibiont Cover/Relocated Seagrass
+ 1.34 acres (0.54 ha) in zones with >33% energy ↓
January 2017
September 2018
4, ~2.5 ac (1.01 ha) Reference Zones
Areas of assessment | % cover 2017 | % cover 2018 | Gain per base (ac/ ha) | Ref. adj change % cover
Reference areas (4, 2.48 ac/ 1.00 ha) | 16% | 20% | 0.22/ 0.09 | 
Total area of >66% wave Energy decrease | 20% | 43% | 1.18/ 0.48 | 22%
Total area of 34-66% wave Energy decrease | 23% | 46% | 1.02/ 0.41 | 18%
Total area of 5-33% wave Energy decrease | 30% | 30% | 0.31/ 0.13 | 6%
>66% energy ↓
33-66% energy ↓
5-33% energy ↓

## Slide 13
Conclusions
Seagrass coverage changes across disturbance gradients
NC seagrass/disturbance well studied and modeled
Manipulation of gradient = changes in seagrass coverage
Reefmaker technology with suspended wavebreak structure:
  Supported new, persistent seagrass cover
  Provided substantial additional Essential Fish Habitat service
Cautiously optimistic - seagrass acreage > mitigation requirements
Continued monitoring to validate and improve forecasting

## Slide 14
Questions?